## Slide 1: Principles of Computers 7th Lecture
Pavel Ježek, Ph.D. pavel.jezek@d3s.mff.cuni.cz

## Slide 2: History
UNIVAC
(1951)
150.000 – 1.500.000 USD

## Slide 3: History
UNIVAC
(1951)
Altair 8800
(1974)
Intel 8080
150.000 – 1.500.000 USD
Bill Gates/Paul Allen
Microsoft BASIC

## Slide 4: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Intel 8080
MOS 6502
150.000 – 1.500.000 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Wozniak

## Slide 5: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Intel 8080
MOS 6502
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak

## Slide 6: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Intel 8080
MOS 6502
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD

## Slide 7: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Atari 2600
(1977)
Atari 800
(1979)
Intel 8080
MOS 6502
MOS 6502
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD
495 USD

## Slide 8: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Atari 2600
(1977)
Atari 800
(1979)
Atari 800XE
(1985)
Intel 8080
MOS 6502
MOS 6502
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD
495 USD
120 USD

## Slide 9: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Atari 2600
(1977)
Atari 800
(1979)
Commodore
ZX Spectrum
Tesla PMD 85
Intel 8080
MOS 6502
6502
Zilog Z80
8080
Atari 800XE
(1985)
MOS 6502
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD
495 USD
120 USD

## Slide 10: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Atari 2600
(1977)
Atari 800
(1979)
Atari 800XE
(1985)
IBM PC
(1981)
Commodore
ZX Spectrum
Intel 8080
MOS 6502
MOS 6502
Intel 8088
Tesla PMD 85
6502
Zilog Z80
8080
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD
495 USD
120 USD
1.565 – 3.100 USD

## Slide 11: History
UNIVAC
(1951)
Altair 8800
(1974)
Apple I
(1976)
Apple II
(1977)
Atari 2600
(1977)
Atari 800
(1979)
Atari 800XE
(1985)
IBM PC
(1981)
PC
2019
Commodore
ZX Spectrum
Intel 8080
MOS 6502
MOS 6502
Intel 8088
Intel i3/i5/i7
Tesla PMD 85
6502
Zilog Z80
8080
150.000 – 1.500.000 USD
666 USD
Bill Gates/Paul Allen
Microsoft BASIC
Steve Jobs
Steve Wozniak
1.200 USD
495 USD
120 USD
1.565 – 3.100 USD

## Slide 12: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
 |  | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code

## Slide 13: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA | 0 $90 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing)

## Slide 14: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 | 0 $90 EIP := EIP + 1 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
Instruction size in bytes

## Slide 15: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 | 0 $90 EIP := EIP + 1 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x
Jump/branch instruction

## Slide 16: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 | 0 $90 EIP := EIP + 1 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x
Jump/branch instruction
16-bit PC → 2 byte argument
32-bit EIP → 4 byte argument

## Slide 17: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 | 0 $90 EIP := EIP + 1 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x
Jump/branch instruction
16-bit PC → 2 byte argument
32-bit EIP → 4 byte argument
6502 is LE CPU arch.
x86 is LE CPU arch.

## Slide 18: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 6502 assembler: NOP | 0 $90 EIP := EIP + 1 Intel assembler: NOP | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 6502 assembler: JMP $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 Intel assembler: JMP xx3xx2xx1xx0h | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x

## Slide 19: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 6502 assembler: NOP | 0 $90 EIP := EIP + 1 Intel assembler: NOP | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 6502 assembler: JMP $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 Intel assembler: JMP xx3xx2xx1xx0h | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x
JMP 00000005h in assembler is 15 bytes in UTF-8 encoding including newline:
In machine code = 5 bytes:
E9 05 00 00 00

## Slide 20: Basic Instructions (6502 vs. x86)
6502 machine code | Intel x86 (IA-32) machine code | Comment
0 $EA PC := PC + 1 6502 assembler: NOP | 0 $90 EIP := EIP + 1 Intel assembler: NOP | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code No operation (just do nothing and continue to next instruction)
0 1 2 $4C xx0 xx1 PC := $xx1xx0 6502 assembler: JMP $xx1xx0 | 0 1 2 3 4 $E9 xx0 xx1 xx2 xx3 EIP := $xx3xx2xx1xx0 Intel assembler: JMP xx3xx2xx1xx0h | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Direct jump to target address x
JMP 00000005h in assembler is 15 bytes in UTF-8 encoding:
In machine code = 5 bytes:
E9 05 00 00 00
x86 assembler (compiler)

## Slide 21: Typical ISA Arithmetic Instructions
MIPS: a := b op c
x86, 6502: a := a op b

## Slide 22: 6502 Registers (Accumulator Architecture)
7 0
A
7 0
X
7 0
Y
0000 0001
7 0
S
P
15 0
PC
7 0
6502: 8-bit CPU with 16-bit logical and physical address spaces (1:1 mapping between logical and physical addresses, i.e. logical address = physical address)

## Slide 23: Load Instructions (6502)
6502 machine code | Comment
0 1 $A9 xx0 A := $xx0 PC := PC + 2 6502 assembler: LDA #$xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Load 8-bit constant $xx0 into A register. (Immediate load instruction)

## Slide 24: Load Instructions (6502)
6502 machine code | Comment
0 1 $A9 xx0 A := $xx0 PC := PC + 2 6502 assembler: LDA #$xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Load 8-bit constant $xx0 into A register. (Immediate load instruction)
0 1 2 $AD xx0 xx1 A := MemReadByte($xx1xx0) PC := PC + 3 6502 assembler: LDA $xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code Read 8-bit value from (16-bit) address $xx1xx0 and load the 8-bit value into A register. (Load from absolute address)

## Slide 25: Load Instructions (6502)
6502 machine code (LDA instruction variants) | Comment
0 1 $A9 xx0 A := $xx0 LDA #$xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code ← Instruction behavior 8-bit immediate load into A register
0 1 2 $AD xx0 xx1 A := MemReadByte($xx1xx0) LDA $xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code ← Instruction behavior 8-bit load from absolute address into A register
6502 machine code (LDX instruction variants) | Comment
0 1 $A2 xx0 X := $xx0 LDX #$xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code ← Instruction behavior 8-bit immediate load into X register
0 1 2 $AE xx0 xx1 X := MemReadByte($xx1xx0) LDX $xx1xx0 | ← Offset from instruction’s start (base) address ← Actual bytes of instruction’s machine code ← Instruction behavior 8-bit load from absolute address into X register

## Slide 26: Load Value Into Register
LDA #$xx
LDA $xxxx
LDX imm/addr
LDY imm/addr
A := xx
A := ($xxxx)^
X := imm/addr
Y := imm/addr
2 different variants implies additional 2 different OPCODEs for LDY!
2 different variants implies 2 different OPCODEs for LDX!

## Slide 27: & Store Value From Register
LDA #$xx
LDA $xxxx
LDX imm/addr
LDY imm/addr
STA $xxxx
STX addr
STY addr
A := xx
A := ($xxxx)^
X := imm/addr
Y := imm/addr
($xxxx)^ := A
($addr)^ := X
($addr)^ := Y

## Slide 28: Copy (Transfer) Value Between Registers
TAX
TXA
TAY
TYA
TSX
TXS
X := A
A := X
Y := A
A := Y
X := S
S := X
LDA #$xx
LDA $xxxx
LDX imm/addr
LDY imm/addr
STA $xxxx
STX addr
STY addr
A := xx
A := ($xxxx)^
X := imm/addr
Y := imm/addr
($xxxx)^ := A
($addr)^ := X
($addr)^ := Y