## Slide 1: Principles of Computers 9th Lecture
Pavel Ježek, Ph.D. pavel.jezek@d3s.mff.cuni.cz

## Slide 3: 6502 CPU: r = a + b + e – (c + d)
TEMP1 = a + b + e
TEMP2 = c + d
r = TEMP1 – TEMP2
LDA $0F01
CLC
ADC $0F02
CLC
ADC $0F05
TAY
LDA $0F03
CLC
ADC $0F04
STA $0108
TYA
SEC
SBC $0108
STA $0F0A
8-bit variables
6502 registers
a + b + e
c + d
A
A
TEMP1 – TEMP2
A
Y
RAM (operating memory)
$0F01
$0F02
$0F03
$0F04
$0F05
$0108
$0F0A
TEMP1
TEMP2
r

## Slide 4: x86 CPU: r = a + b + e – (c + d)
x86 registers
TEMP1 = a + b + e
TEMP2 = c + d
r = TEMP1 – TEMP2
a + b + e
c + d
AL
TEMP1 – TEMP2
BL
RAM (operating memory)
$00000F01
$00000F02
$00000F03
$00000F04
$00000F05
MOV AL, [00000F01h]
ADD AL, [00000F02h]
ADD AL, [00000F05h]
MOV BL, [00000F03h]
ADD BL, [00000F04h]
SUB AL, BL
MOV [00000F0Ah], AL
$00000F0A
8-bit variables
TEMP1
TEMP2

## Slide 5: x86 CPU: r = a + b + e – (c + d)
x86 registers
TEMP1 = a + b + e
TEMP2 = c + d
r = TEMP1 – TEMP2
a + b + e
c + d
EAX
TEMP1 – TEMP2
EBX
RAM (operating memory)
$00000F00
$00000F04
$00000F08
$00000F0C
$00000F10
MOV EAX, [00000F00h]
ADD EAX, [00000F04h]
ADD EAX, [00000F10h]
MOV EBX, [00000F08h]
ADD EBX, [00000F0Ch]
SUB EAX, EBX
MOV [00000F20h], EAX
$00000F20
32-bit variables
TEMP1
TEMP2

## Slide 7: Instruction Timing

## Slide 8: Speed of Addition (32-bit vs. 64-bit + Python vs. C/C#)

## Slide 9: No Division (div), No Mutiplication (*) Instructions on 6502

## Slide 10: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
32
16
8
4
2
1
SHL 1
* 2

## Slide 11: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
= 1*23+1 + 1*21+1 + 1*20+1
= (1*23 + 1*21 + 1*20) * 21
32
16
8
4
2
1
SHL 1
* 2

## Slide 12: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
= 1*23+1 + 1*21+1 + 1*20+1
= (1*23 + 1*21 + 1*20) * 21
32
16
8
4
2
1
SHL 1
5
4
3
2
1
0
000101
101000
= 5 = 1*22 + 1*20
= 40 = 1*25 + 1*23
32
16
8
4
2
1
SHL 3
* 2
* 8

## Slide 13: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
= 1*23+1 + 1*21+1 + 1*20+1
= (1*23 + 1*21 + 1*20) * 21
32
16
8
4
2
1
SHL 1
5
4
3
2
1
0
000101
101000
= 5 = 1*22 + 1*20
= 40 = 1*25 + 1*23
= 1*22+3 + 1*20+3
= (1*22 + 1*20) * 23
32
16
8
4
2
1
SHL 3
* 2
* 8

## Slide 14: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
= 1*23+1 + 1*21+1 + 1*20+1
= (1*23 + 1*21 + 1*20) * 21
32
16
8
4
2
1
SHL 1
5
4
3
2
1
0
000101
101000
= 5 = 1*22 + 1*20
= 40 = 1*25 + 1*23
= 1*22+3 + 1*20+3
= (1*22 + 1*20) * 23
32
16
8
4
2
1
SHL 3
* 2
* 8
x SHL n
x * 2n

## Slide 15: Shift Left << (Unsigned Integers)
5
4
3
2
1
0
001011
010110
= 11 = 1*23 + 1*21 + 1*20
= 22 = 1*24 + 1*22 + 1*21
= 1*23+1 + 1*21+1 + 1*20+1
= (1*23 + 1*21 + 1*20) * 21
32
16
8
4
2
1
SHL 1
5
4
3
2
1
0
000101
101000
= 5 = 1*22 + 1*20
= 40 = 1*25 + 1*23
= 1*22+3 + 1*20+3
= (1*22 + 1*20) * 23
32
16
8
4
2
1
SHL 3
* 2
* 8
x SHL n
(x * 2n) MOD 2z
z-bit precission

## Slide 16: Shift Right >> (Unsigned Integers)
5
4
3
2
1
0
001011
000101
= 11 = 1*23 + 1*21 + 1*20
= 5 = 1*22 + 1*20
32
16
8
4
2
1
SHR 1
DIV 2

## Slide 17: Shift Right >> (Unsigned Integers)
5
4
3
2
1
0
001011
000101
= 11 = 1*23 + 1*21 + 1*20
= 5 = 1*22 + 1*20
= 1*23-1 + 1*21-1 + 1*20-1
= (1*23 + 1*21 + 1*20) / 21
32
16
8
4
2
1
SHR 1
DIV 2

## Slide 18: Shift Right >> (Unsigned Integers)
5
4
3
2
1
0
001011
000101
= 11 = 1*23 + 1*21 + 1*20
= 5 = 1*22 + 1*20
= 1*23-1 + 1*21-1 + 1*20-1
= (1*23 + 1*21 + 1*20) / 21
32
16
8
4
2
1
SHR 1
DIV 2
2-1 = 0.5

## Slide 19: Shift Right >> (Unsigned Integers)
5
4
3
2
1
0
001011
000101
= 11 = 1*23 + 1*21 + 1*20
= 5 = 1*22 + 1*20
= 1*23-1 + 1*21-1 + 1*20-1
= (1*23 + 1*21 + 1*20) / 21
32
16
8
4
2
1
SHR 1
5
4
3
2
1
0
010010
000010
= 18 = 1*24 + 1*21
= 2 = 1*21
= 1*24-3 + 1*21-3
= (1*24 + 1*21) / 23
32
16
8
4
2
1
SHR 3
DIV 2
DIV 8
2-1 = 0.5
2-2 = 0.25

## Slide 20: Shift Right >> (Unsigned Integers)
5
4
3
2
1
0
001011
000101
= 11 = 1*23 + 1*21 + 1*20
= 5 = 1*22 + 1*20
= 1*23-1 + 1*21-1 + 1*20-1
= (1*23 + 1*21 + 1*20) / 21
32
16
8
4
2
1
SHR 1
5
4
3
2
1
0
010010
000010
= 18 = 1*24 + 1*21
= 2 = 1*21
= 1*24-3 + 1*21-3
= (1*24 + 1*21) / 23
32
16
8
4
2
1
SHR 3
DIV 2
DIV 8
x SHR n
x DIV 2n
2-1 = 0.5
2-2 = 0.25

## Slide 21: Shift Left << (Signed Integers)
5
4
3
2
1
0
111011
110110
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
NOT(result) = 0 0 1 0 0 1
NOT(result)+1 = 0 0 1 0 1 0
= 8 + 2 = 10 → -10
32
16
8
4
2
1
SHL 1
* 2

## Slide 22: Shift Left << (Signed Integers)
5
4
3
2
1
0
111011
110110
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
NOT(result) = 0 0 1 0 0 1
NOT(result)+1 = 0 0 1 0 1 0
= 8 + 2 = 10 → -10
32
16
8
4
2
1
SHL 1
5
4
3
2
1
0
111011
011000
= -5
= 16 + 8 = 24 😒
32
16
8
4
2
1
SHL 3
* 2
* 8
x SHL n
x * 2n
if small enough

## Slide 23: Logical Shift Right >> (Signed Integers)
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
5
4
3
2
1
0
111011
011101
= 16 + 8 + 4 + 1 = 29
32
16
8
4
2
1
SHR 1
DIV 2
x SHR n
x DIV 2n
NO!

## Slide 24: Arithmeric Shift Right >> (Signed Integers)
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
5
4
3
2
1
0
111011
111101
NOT(result) = 0 0 0 0 1 0
NOT(result)+1 = 0 0 0 0 1 1
= 2 + 1 = 3 → -3
32
16
8
4
2
1
SAR 1
almost
DIV 2

## Slide 25: Arithmeric Shift Right >> (Signed Integers)
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
5
4
3
2
1
0
111011
111101
NOT(result) = 0 0 0 0 1 0
NOT(result)+1 = 0 0 0 0 1 1
= 2 + 1 = 3 → -3
32
16
8
4
2
1
SAR 1
almost
DIV 2
5
4
3
2
1
0
111010
111101
= -6
NOT(result) = 0 0 0 0 1 0
NOT(result)+1 = 0 0 0 0 1 1
= 2 + 1 = 3 → -3
32
16
8
4
2
1
SAR 1
DIV 2

## Slide 26: Arithmeric Shift Right >> (Signed Integers)
5 = 0 0 0 1 0 1
NOT(x) + 1 = 1 1 1 0 1 0 + 1
= -5
5
4
3
2
1
0
111011
111101
NOT(result) = 0 0 0 0 1 0
NOT(result)+1 = 0 0 0 0 1 1
= 2 + 1 = 3 → -3
32
16
8
4
2
1
SAR 1
almost
DIV 2
x SAR n
x DIV 2n
5
4
3
2
1
0
111010
111101
= -6
NOT(result) = 0 0 0 0 1 0
NOT(result)+1 = 0 0 0 0 1 1
= 2 + 1 = 3 → -3
32
16
8
4
2
1
SAR 1
DIV 2